## Slide 1
SAFMIs: Segmented Atomic Force Microscope Images
Demi Liu1,4, Sarthak P. Jariwala2,4, Christopher Nyambura3, Sid Rath2,5
1. Chemistry 2. Material Science and Engineering 3. Chemical Engineering 4. CEI 5. GEMSEC
Background Subtraction
Image Segmentation: Random Walk
Random walker segmentation from scikit-image was employed for this step. Random walk solves an anisotropic diffusion equation with tracers starting from a pre-determined pixel with a certain label (initial marker position). Diffusivity is high, if neighboring pixels have similar values, whereas widely varying pixels values results in low diffusion. Thus, diffusion has a inverse relationship to the gradient height.
Prediction of Bio/Nano Interface Parameters using KNN Clustering and Regression
The background approximation and subtraction function uses Morphological Filtering from scikit-image. It returns all bright spots in the image that are smaller than the structuring element that the user defines (rectangular, square or ellipsoidal/circular). It outputs a foreground with some threshold, deletes the background, while preserving the relative height values to use later.
Generation of Image Descriptors from Segmented Images
Images provided by:
David Starkebaum (affiliation: GEMSEC)
Tyler Dean Jorgenson (affiliation: GEMSEC)
Percentile Filter from scikit-ndimage module allowed for separation of ordered and disordered ratios. Furthermore, a percent coverage was calculated; these two parameters are image descriptors that are specific to the experimental conditions of the surface under the microscope
K-Nearest Neighbor Clustering was performed on 50 images where a random test/train split was performed. Images were clustered based on pH and concentration of the peptide solution used to create the bio-interface observed under AFM. Next, regression was used to predict order/disorder ratio and percent coverage for a given input AFM image with the same clustering parameters.
Special Thanks to:
Prof Mehmet Sarikaya
PI: GEMSEC (NSF-MGI Program)
Acknowledgments:
Dr. David Beck
Nicholas Montoni
Arushi Prakash
Moke Mao